memo

ヒーター：
　電力・燃料などで投入したエネルギを，熱に変換

灯油などの燃料/電力
(エネルギ投入)

熱
(室温上昇に使う)

ヒーター
燃焼，電熱線など

投入エネルギ ≧ 室温を上げる熱

Fuel/Electricity
(energy input)
Heater:
Combustion, heating wire, etc

Heat
(contributes warming room temperature)
Energy input ≧ Heat which warm the room
∵Heat source == energy input

Work
(energy input)
Heat
(contributes warming room temperature)

Heat that outside air has.
(even it is “cold”, there is heat (or energy) in it)

Heat pump

Energy input ＜ Heat which warm the room
∵Heat souce == outside air

動力
(エネルギ投入)

熱
(室温上昇に使う)

外気が持つ熱
(”冷た”くても熱量は有している)
ヒートポンプ

投入エネルギ ＜ 室温を上げる熱

Heating by heater.
Heating by Air Conditioner (heat pump).

Stop heating operation when temperature reaches target.

Room. Assumed heat insulated closed volume.

Heater: just add heat into room..
Heat pump: ideal Carnot heat pumping cycle machine..
Heat taken from outside air and carried into room, instead of burning fuel/electrical heating...
Pumping heat requires some work. (driving power)

Heat pump, =エアコン, の方が圧倒的に少ない投入エネルギで室温を上昇させられる．
副次的な作用として，Heat pumpは外気をより低温にする．
ただし，地球全体で見ると，heat pumpに投入した仕事が熱に変わった分，より”熱く”なっている．

Heater: just add heat into room..